## Slide 1: Module 5: Number Systems
Introduction to Networks v7.0 (ITN)
Notes: Cisco Networking Academy Program
Introduction to Networks v7.0 (ITN)
Module 5: Number Systems

## Slide 2: Module Objectives
Module Title: Number Systems
Module Objective: Calculate numbers between decimal, binary, and hexadecimal systems.
Topic Title | Topic Objective
Binary Number System | Calculate numbers between decimal and binary systems.
Hexadecimal Number System | Calculate numbers between decimal and hexadecimal systems.
Notes: 2
5.0- Introduction
5.0.2 – What will I learn in this module?

## Slide 3: 5.1 Binary Number System
Notes: 5 -Number Systems
5.1 Binary Number System

## Slide 4: Binary Number System Binary and IPv4 Addresses
Binary numbering system consists of 1s and 0s, called bits
Decimal numbering system consists of digits 0 through 9
Hosts, servers, and network equipment using binary addressing to identify each other.
Each address is made up of a string of 32 bits, divided into four sections called octets.
Each octet contains 8 bits (or 1 byte) separated by a dot.
For ease of use by people, this dotted notation is converted to dotted decimal.
Notes: 5 – Number Systems
5.1 – Binary Number Systems
5.1.1 – Binary and IPv4 Addresses

## Slide 5: Binary Number System Decimal Positional Notation
Positional notation means that a digit represents different values depending on the “position” the digit occupies in the sequence of numbers.
The decimal positional notation system operates as shown in the tables below.
Radix | 10 | 10 | 10 | 10
Position in Number | 3 | 2 | 1 | 0
Calculate | (103) | (102) | (101) | (100)
Position Value | 1000 | 100 | 10 | 1
 | Thousands | Hundreds | Tens | Ones
Positional Value | 1000 | 100 | 10 | 1
Decimal Number (1234) | 1 | 2 | 3 | 4
Calculate | 1 x 1000 | 2 x 100 | 3 x 10 | 4 x 1
Add them up… | 1000 | + 200 | + 30 | + 4
Result | 1,234 |  |  | 
Notes: 5 – Number Systems
5.1 – Binary Number Systems
5.1.3 – Binary Positional Notation

## Slide 6: Binary Number System Binary Positional Notation (Cont.)
The binary positional notation system operates as shown in the tables below.
Radix | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
Position in Number | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Calculate | (27) | (26) | (25) | (24) | (23) | (22) | (21) | (20)
Position Value | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
Positional Value | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
Binary Number (11000000) | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
Calculate | 1x128 | 1x64 | 0x32 | 0x16 | 0x8 | 0x4 | 0x2 | 0x1
Add Them Up… | 128 | + 64 | + 0 | + 0 | + 0 | + 0 | + 0 | + 0
Result | 192 |  |  |  |  |  |  | 
Notes: 5 – Number Systems
5.1 – Binary Number Systems
5.1.3 – Binary Positional Notation
5.1.4 – Check Your Understanding – Binary Number System

## Slide 7: Binary Number System Convert Binary to Decimal
Convert 11000000.10101000.00001011.00001010 to decimal.
Positional Value | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
Binary Number (11000000) | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
Calculate | 1x128 | 1x64 | 0x32 | 0x16 | 0x8 | 0x4 | 0x2 | 0x1
Add Them Up… | 128 | + 64 | + 0 | + 0 | + 0 | + 0 | + 0 | + 0
Binary Number (10101000) | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0
Calculate | 1x128 | 0x64 | 1x32 | 0x16 | 1x8 | 0x4 | 0x2 | 0x1
Add Them Up… | 128 | + 0 | + 32 | + 0 | + 8 | + 0 | + 0 | + 0
Binary Number (00001011) | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1
Calculate | 0x128 | 0x64 | 0x32 | 0x16 | 1x8 | 0x4 | 1x2 | 1x1
Add Them Up… | 0 | + 0 | + 0 | + 0 | + 8 | + 0 | + 2 | + 1
Binary Number (00001010) | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
Calculate | 0x128 | 0x64 | 0x32 | 0x16 | 1x8 | 0x4 | 1x2 | 0x1
Add Them Up… | 0 | + 0 | + 0 | + 0 | + 8 | + 0 | + 2 | + 0
192
168
11
10
192.168.11.10
Notes: 5 – Number Systems
5.1 – Binary Number Systems
5.1.5 - Convert Binary to Decimal
5.1.6 – Activity – Binary to Decimal Conversions

## Slide 8: Binary Number System Decimal to Binary Conversion
The binary positional value table is useful in converting a dotted decimal IPv4 address to binary.
    Start in the 128 position (the most significant bit). Is the decimal number of the octet (n) equal to or greater than 128?
    If no, record a binary 0 in the 128 positional value and move to the 64 positional value.
    If yes, record a binary 1 in the 128 positional value, subtract 128 from the decimal number, and move to the 64 positional value.
    Repeat these steps through the 1 positional value.
Notes: 5 – Number Systems
5.1 – Binary Number Systems
5.1.7 – Decimal to Binary Conversion

## Slide 9: Binary Number System Decimal to Binary Conversion Example
Convert decimal 168 to binary
Is 168 > 128?
Yes, enter 1 in 128 position and subtract 128 (168-128=40)
Is 40 > 64?
No, enter 0 in 64 position and move on
Is 40 > 32?
Yes, enter 1 in 32 position and subtract 32 (40-32=8)
Is 8 > 16?
No, enter 0 in 16 position and move on
Is 8 > 8?
Equal. Enter 1 in 8 position and subtract 8 (8-8=0)
No values left. Enter 0 in remaining binary positions
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 0 | 1 | 0 | 1 | 0 | 0 | 0
Decimal 168 is written as 10101000 in binary
Notes: 5 – Number Systems
5.1 – Binary Number Systems
5.1.8 – Decimal to Binary Conversion Example
5.1.9 - Activity – Decimal to Binary Conversions
5.1.10 – Activity – Binary Game

## Slide 10: Binárne čísla - prevody
10
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
10 na bin (1010)
10:2=5 zv 0
5:2=2 zv 1
2:2=1 zv 0
1:2=0 zv 1
9 Bin 1 0 0 1
1101 na dec
1*8+1*4+0*2+1*1=13

## Slide 11
128-64-32-16-8-4-2-1

## Slide 12: Binary Number System IPv4 Addresses
Routers and computers only understand binary, while humans work in decimal. It is important for you to gain a thorough understanding of these two numbering systems and how they are used in networking.
SM 11111111
255
11111111
255
11111111
255
00000000
0
Notes: 5 – Number Systems
5.1 – Binary Number Systems
5.1.11 – IPv4 Addresses

## Slide 13: 5.2 Hexadecimal Number System
Notes: 5- Number Systems
5.2 - Hexadecimal Number System

## Slide 14: Hexadecimal Number System Hexadecimal and IPv6 Addresses
To understand IPv6 addresses, you must be able to convert hexadecimal to decimal and vice versa.
Hexadecimal is a base sixteen numbering system, using the digits 0 through 9 and letters A to F.
It is easier to express a value as a single hexadecimal digit than as four binary bit.
Hexadecimal is used to represent IPv6 addresses and MAC addresses.
Notes: 5 – Number Systems
5.2 – Hexadecimal Number Systems
5.2.1– Hexadecimal and IPv6 Addresses

## Slide 15: Hexadecimal Number System Hexadecimal and IPv6 Addresses (Cont.)
IPv6 addresses are 128 bits in length. Every 4 bits is represented by a single hexadecimal digit. That makes the IPv6 address a total of 32 hexadecimal values.
The figure shows the preferred method of writing out an IPv6 address, with each X representing four hexadecimal values.
Each four hexadecimal character group is referred to as a hextet.
Notes: 5 – Number Systems
5.2 – Hexadecimal Number Systems
5.2.1– Hexadecimal and IPv6 Addresses

## Slide 16: Hexadecimal Number System Decimal to Hexadecimal Conversions
Follow the steps listed to convert decimal numbers to hexadecimal values:
Convert the decimal number to 8-bit binary strings.
Divide the binary strings in groups of four starting from the rightmost position.
Convert each four binary numbers into their equivalent hexadecimal digit.
For example, 168 converted into hex using the three-step process.
168 in binary is 10101000.
10101000 in two groups of four binary digits is 1010 and 1000.
1010 is hex A and 1000 is hex 8, so 168 is A8 in hexadecimal.
Notes: 5 – Number Systems
5.2 – Hexadecimal Number Systems
5.2.3 – Decimal to Hexadecimal Conversions

## Slide 17: Hexadecimal Number System Hexadecimal to Decimal Conversions
Follow the steps listed to convert hexadecimal numbers to decimal values:
Convert the hexadecimal number to 4-bit binary strings.
Create 8-bit binary grouping starting from the rightmost position.
Convert each 8-bit binary grouping into their equivalent decimal digit.
For example, D2 converted into decimal using the three-step process:
D2 in 4-bit binary strings is 1110 and 0010.
1110 and 0010 is 11100010 in an 8-bit grouping.
11100010 in binary is equivalent to 210 in decimal, so D2 is 210 is decimal
Notes: 5 – Number Systems
5.2 – Hexadecimal Number Systems
5.2.4 - Hexadecimal to Decimal Conversions
5.2.5 – Check Your Understanding – Hexadecimal Number System

## Slide 18: Hexadecimálne čísla – prevody (0123456789ABCDEF)
300 na hex
300:16=18 zv 12
18:16=1 zv 2
300 0x1 2 C
2F1 na dec
2*256+15*16+1*1=753
4096 | 256 | 16 | 1
163 | 162 | 161 | 160

## Slide 19
8-4-2-1 A10B11C12D13E14F15